## Slide 1
Dynamic Modeling and UQ Workflow
Dynamic Modeling and Intrusive Uncertainty Quantification (UQ) for Membrane Separation Systems
Keshav Kasturi Rangan, Molly Dougher, Laurianne Estrada, Shammah Lilonfe, Pratham Singh, William A. Phillip, Alexander W. Dowling Department of Chemical and Biomolecular Engineering, University of Notre Dame
Email: kkasturi@nd.edu
Takeaways
Pyomo workflow for intrusive UQ and MBDoE using ParmEst, Pyomo.DoE
MBDoE is similar to optimal control with an information objective instead of performance
    General control:
    MBDoE:
Derivative-consistent sensitivities enable identifiability and model discrimination in membrane transport
Closed-loop input design
    Estimate → Quantify → Design → Repeat; until target uncertainty is reached
Motivation
Objective
Impactful applications
  Water treatment
  Chemical manufacturing
  Critical-material recovery
Membrane systems modeling limitations
  Uncertainty in transport models
  Poor parameter identifiability
Impact on process design
  Degraded prediction accuracy
  Unreliable scalability
References
1 Wang, J., & Dowling, A. W. (2022). Pyomo. DOE: An open‐source package for model‐based design of experiments in Python. AIChE Journal, 68(12), e17813.
2 Liu, X., Estrada, L., Ouimet, J. A., McClure, M., Latulippe, D. R., Phillip, W. A., & Dowling, A. W. (2025). Characterizing Transport Properties of Surface Charged Nanofiltration Membranes via Model-Based Data Analytics. Industrial & Engineering Chemistry Research.
Optimize the identification of the most-informative operating conditions
  Develop a dynamic, equation-oriented model using experimental data
  Compute model-consistent uncertainty using intrusive derivatives
  Design the next experiment to maximally reduce uncertainty
Validate using a membrane separation experiment and generalize
Mechanistic Dynamic Model
Parameter Estimation
Operating Condition: MBDoE
Stopping Criterion
Intrusive UQ: Covariance/FIM
Legend
states
: inputs
operating conditions
: transport parameters
: parameter estimate
: measured output,
: noise
measurement covariance
: sensitivity (UQ)
: FIM
: sequential experiment index
: feasible design space
Prior
Knowledge
Model(s)
Uncertainty Acceptable?
Model with Quantified Uncertainty
No
Yes
Sensitivity & Uncertainty Analysis
ParmEst
ParmEst
Parameter Estimation
Model-Based Design of Experiments
Experimental Data
D‑optimality (maximize ) metric
A‑optimality: minimize
E/ME‑optimality: worst‑case directions
Both trends are consistent
Weighted Sum of
Squared Errors (WSSE)
Central Finite Difference
LinkedIn