## Slide 1
High-throughput experiments elucidate the impact of multicomponent interactions on solute transport in complex feed streams.
Target Journal: Nature Water
Experimental Results - 5/11/2024
Laurianne Estrada, Jonathan A. Ouimet, Zhicheng Lu, Molly Dougher, Shammah Lilonfe, Alexander Dowling, William Phillip

## Slide 2
Overarching Questions/Goals for Today
Reminder to experiments available.
  What data is being collected throughout the course of these experiments?
  How is this data analyzed to constrain the conductivity readings and monitor the concentration of ions in the feed and permeate?
Modeling efforts
  Single component – Planning/discussion/timeline
  Multicomponent systems
    Concentration polarization
    Solute Transport in membranes with Donnan
  Experiments will focus on Na+ | Ca2+ | La3+ separations due to there importance in refining ores and recycling electronics.

## Slide 3
Diafiltration Experiments are Run in a Modified Stirred Cell Apparatus.
Membrane
Retentate Probe
Permeate Probe
Scintillation Vials
Motor
Balance
Pressure Gauge
P
Diafiltrate Tank
Pressure Relief Valve
Stirred Cell
Permeate Outlet
Multiple (two) salts are now placed within the feed and diafiltrate reservoirs.
Retentate and permeate conductivity data are obtained at 5 second intervals.
Scintillation vials are analyzed after the experiment (ICP-OES) to get ion specific concentrations.

## Slide 4
RAW Excel Data will be Included in the Supplementary Information.

## Slide 5
Data Analysis and Visualization
Feed: 20 mM NaCl
Diafiltrate: 10 mM NaCl, 50 mM CaCl2

## Slide 6
Single Salt Experiments - Running these will mirror Xinhong’s work for the “Permeate Probe” and “NF270” Manuscripts.
  Who in the Dowling lab is running these to regress variables?
  Do we have a code that is functional for single component data analysis
    That simultaneously regresses parameters using (1) retentate and permeate conductivity probes, (2) ICP data, (3) mass data
  What is the timeline to get the single salt experiments rigorously analyzed through the codes?
    Regression of H, D, Lp, σ, identification of which salts possess concentration dependent parameters?
    Let’s email to set up a meeting offline.
Multicomponent Experiments
  Analysis was limited by my derivation of multicomponent equations.
Action Items/Discussion

## Slide 7
Request/Need: Everything needs to be in BOX for me to follow along.
Over 28 experiments have been conducted to characterize multicomponent effects.
Single Salt Experiments: 13 Experiments (7 NaCl, 4 CaCl2, 2 LaCl3)
Two Salt Experiments: 15 Experiments

## Slide 8
Physical picture of modeling efforts.
Membrane
Feed
Permeate
Concentration Polarization
Partitioning
Membrane Transport/Diffusion
Concentration polarization
Nernst Plank Equation
Electroneutrality Constraint.
Solute Partitioning
NF270 Manuscript
… relate to Donnan equilibrium (or similar model)
Membrane Transport/Diffusion
Nernst Plank Equation
Electroneutrality Constraint.

## Slide 9
Equations for the flux of species in solution.
Derived from Nernst-Plank equation, two species in solution.
Nernst-Plank Equation.
Electroneutrality Constraint.
,
…Solving provides an equation for the flux of ions.
Concentration Polarization
Analytical Solution.

## Slide 10
Equations for the flux of species in solution.
Derived from Nernst-Plank equation, three species in solution.
Nernst-Plank Equation.
Electroneutrality Constraint.
,
Be cautious about negative and positive signs. Please check derivation to ensure accuracy.
…Solving provides an equation for the flux of ions.

## Slide 11
Equations for the flux of species in solution.
Derived from Nernst-Plank equation, three species in solution.
Concentration Polarization
Solve using matrix algebra
Known variables:
Volumetric water flux:
Bulk retentate and permeate concentrations:
Unknown Variables:
Boundary layer thickness:
Interface concentrations:
Be cautious about negative and positive signs. Please check derivation to ensure accuracy.
No analytical solution exists.
Estimate bound by single species estimates (additional variable)
Select an average of the single species boundary layer
** We can solve the differential equations with the initial conditions.

## Slide 12
Equations for the flux of species in solution.
Derived from Nernst-Plank equation, three species in solution.
Within one of the diafiltration experiments:
** Solve the differential equations with respect to position.
This does not give us an interface concentration, we arbitrarily chose a boundary layer thickness of 100 µm
Estimate boundary layer thickness using the diffusion coefficient of each ion in solution.

## Slide 13
Physical picture of modeling efforts.
Membrane
Feed
Permeate
Concentration Polarization
Partitioning
Membrane Transport/Diffusion
Concentration polarization
Nernst Plank Equation
Electroneutrality Constraint.
Solute Partitioning
NF270 Manuscript
… relate to Donnan equilibrium (or similar model)
Membrane Transport/Diffusion
Nernst Plank Equation
Electroneutrality Constraint.

## Slide 14
Solute Partitioning: Donnan equilibrium.
The chemical potential of species ‘i’ is equal in the membrane and in the solution.
Use electroneutrality constraint.
… use a solver to obtain the concentration of solute in the membrane.
Representative of a NaCl/LaCl3 System
Specie 1: +1
Specie 2: +3
Specie 3: -1

## Slide 15
Physical picture of modeling efforts.
Membrane
Feed
Permeate
Concentration Polarization
Partitioning
Membrane Transport/Diffusion
Concentration polarization
Nernst Plank Equation
Electroneutrality Constraint.
Solute Partitioning
NF270 Manuscript
… relate to Donnan equilibrium (or similar model)
Membrane Transport/Diffusion
Nernst Plank Equation
Electroneutrality Constraint.

## Slide 16
Membrane transport derived for multicomponent transport in membranes.
Nernst-Plank Equation.
Electroneutrality Constraint.
, ,
…Solving provides an equation for the flux of ions.

## Slide 17
Single Salt Experiments - Running these will mirror Xinhong’s work for the “Permeate Probe” and “NF270” Manuscripts.
  Who in the Dowling lab is running these to regress variables?
  Do we have a code that is functional for single component data analysis
    That simultaneously regresses parameters using (1) retentate and permeate conductivity probes, (2) ICP data, (3) mass data
  What is the timeline to get the single salt experiments rigorously analyzed through the codes?
    Regression of H, D, Lp, σ, identification of which salts possess concentration dependent parameters?
    Let’s email to set up a meeting offline.
Multicomponent Experiments
  Analysis was limited by my derivation of multicomponent equations.
    Equations are available online BOX.
    Jonathan/Laurianne Action Item: Need to clean up derivation to include in SI.
  Once single salt is done, I will reach out to set up a meeting for multicomponent regression.
Action Items/Discussion

## Slide 18
Supplementary Slides

## Slide 19
Manuscript Figures

## Slide 20
Figure 1
Membrane
Retentate Probe
Permeate Probe
Scintillation Vials
Motor
Balance
Pressure Gauge
P
Diafiltrate Tank
Pressure Relief Valve
Stirred Cell
Permeate Outlet
Combine Figure 1 and 2?

## Slide 21
Figure 2
NaCl – Single Component raw data

## Slide 22
Figure 3
*Main text will show NaCl/LaCl3. SI plots can be made for NaCl/CaCl2 and CaCl2/LaCl3 multicomponent salts.
NaCl + LaCl3 multicomponent raw data

## Slide 23
Figure 4
Add a circle for the feed concentration (experiment start).
Add a star for the retentate concentration (experiment ends).
Triangles are retentate concentrations that correspond to each permeate vial (calculated from a mass balance using ICP).

## Slide 24
Figure 5

## Slide 25
Figure 6
Three ion experiment provided by model-based design of experiments.
Raw diafiltration data
Ion rejections
Selectivity
Material Properties

## Slide 26
Figure S#

## Slide 27
Supplementary Slides

## Slide 28
SI Table with all the experiments – operating conditions, feed and diafiltrate concentrations, etc.
SI Figures for all experiments conducted to visualize/verify agreement between multiple types of data: Total of 15 – 20 sets of figures. (Duplicate experiments will not have figures)
Edits to figure.
Right panel: The current shapes are too similar – suggest having unfilled/half filled diamonds.
Left panel: The green diamonds are ‘confusing’. These are predictions, they should be a line.
NF270_MC2, E2. Feed: 20 mM CaCl2, Diafiltrate: 8 mM CaCl2, 50 mM NaCl

## Slide 29
CaCl2 – Single Component
LaCl3 – Single Component

## Slide 30
NaCl – CaCl2 Multicomponent
E1.
Feed: 10 mM CaCl2
Diafiltrate: 50 mM NaCl, 4 mM CaCl2
E2.
Feed: 20 mM CaCl2
Diafiltrate: 50 mM NaCl, 8 mM CaCl2
E3.
Feed: 10 mM NaCl
Diafiltrate: 50 mM CaCl2, 5 mM NaCl
E4.
Feed: 20 mM NaCl
Diafiltrate: 50 mM CaCl2, 10 mM NaCl
E5.
Feed: 10 mM NaCl, 1 mM CaCl2
Diafiltrate: 50 mM CaCl2, 50 mM NaCl